## Slide 1
01
Smart Parking
Slot Availability & Entry Control System
Design and Simulation using Combinational Logic
MODULE 2 • MAKING DECISIONS & DOING MATHS
Team Members
2620030353 • 2620030358 2620030363 • 2620030366

## Slide 2
02
Project Overview
A simple digital system for smarter parking
Detects whether each parking slot is occupied or free.
Shows parking availability using logic outputs or indicator LEDs.
Allows entry only when at least one slot is available.
Uses combinational logic: outputs depend only on current inputs.
INPUTS → LOGIC CIRCUIT → STATUS + ENTRY

## Slide 3
03
Problem Statement
Why is this system useful?
Drivers may waste time searching for an empty slot.
Manual entry control can cause confusion and congestion.
A logic-based controller can instantly indicate availability.
The design is small, low-cost, and suitable for simulation.

## Slide 4
04
Objectives
What the project aims to achieve
Represent parking slots with binary inputs.
Determine availability using Boolean logic.
Generate an AVAILABLE / FULL output.
Control the entry signal using the availability result.
Test input combinations in a simulator.

## Slide 5
05
Module 2 Connection
Combinational Logic & the ALU
Combinational logic has no memory; outputs depend on current inputs.
Boolean expressions describe the parking decision.
Truth tables list every input combination and its output.
K-maps can simplify expressions and reduce gate count.
The same logic-gate principles are used inside a CPU's ALU.

## Slide 6
06
Inputs & Outputs
A 3-slot example for easy simulation
INPUTS
A = 1 if Slot A is occupied; 0 if free
B = 1 if Slot B is occupied; 0 if free
C = 1 if Slot C is occupied; 0 if free
OUTPUTS
AVAILABLE = 1 when at least one slot is free
FULL = 1 when all three slots are occupied
ENTRY = 1 only when AVAILABLE = 1

## Slide 7
07
Boolean Logic Design
Occupied inputs use active-high logic
FULL = A · B · C
AVAILABLE = ¬(A · B · C)
ENTRY = AVAILABLE · REQUEST
REQUEST = 1 when a vehicle is waiting to enter.
· = AND ¬ = NOT

## Slide 8
08
Truth Table
For three parking slots
A | B | C | FULL | AVAILABLE
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 9
09
Circuit Design
Build with basic gates in Logisim
A, B, C
AND Gate
NOT Gate
AND output = FULL; NOT output = AVAILABLE
ENTRY = AVAILABLE AND REQUEST
Add LEDs to represent FULL, AVAILABLE, and ENTRY.

## Slide 10
10
Logic Simplification
Using Boolean algebra and K-map ideas
FULL = A · B · C is a simple three-input AND expression.
AVAILABLE = ¬(A · B · C) can be implemented with a NAND gate.
A NAND gate combines AND and NOT in one component.
Fewer gates can reduce circuit size, cost, and power.

## Slide 11
11
Simulation & Testing
Verify the design in Logisim Evolution
Place three input switches for A, B, and C.
Connect them to a 3-input AND gate to generate FULL.
Invert FULL to generate AVAILABLE.
Connect AVAILABLE and REQUEST to an AND gate for ENTRY.
Test all 8 combinations and confirm the truth table.

## Slide 12
12
Applications & Future Scope
Where this design can be extended
Small shopping centres, offices, and campus parking areas.
Add sensors to detect vehicles automatically.
Display the number of free slots using a counter.
Extend to more slots with grouped logic or a decoder.
Add a barrier motor and entry/exit counting in a future version.

## Slide 13
13
Conclusion
A small project with a real-world purpose
The system identifies whether parking is FULL or AVAILABLE.
Entry is permitted only when a slot is free and a vehicle requests entry.
The circuit demonstrates combinational logic, Boolean expressions, and truth tables.
The final circuit can be simulated and tested using Logisim Evolution.
THANK YOU