## Slide 1
DDCA PROJECT · KL UNIVERSITY
Simulation of an Intelligent Traffic Signal Controller Using FSM
A clocked digital controller for safe, repeatable traffic flow.
Section: 14
Team: 8
2620030353;
2620030358;
2620030358;
2620030366

## Slide 2
SYSTEM OVERVIEW
Safe traffic control starts with one shared clock
An intelligent traffic signal controller coordinates two intersecting roads through timed digital states.
One clock
Each clock edge advances the controller in a known order.
One FSM
The current state determines the next transition and outputs.
One safety rule
Conflicting green lights are never allowed.
Objectives: automate signal changes, control traffic flow, prevent conflicting green lights, and demonstrate digital logic in Logisim.
2

## Slide 3
FINITE STATE MACHINE
Five states turn timing into safe, repeatable logic
The clock advances the FSM; D flip-flops store the state; AND, OR, and NOT gates form next-state and output logic.
S0
Main green · side red
S1
Main yellow · side red
S2
Both roads red · all-red clearance interval
S3
Main red · side green
S4
Main red · side yellow
Clocked sequence: S0 → S1 → S2 → S3 → S4 → S2 → S0
CLOCK
Advance
STATE REGISTER
D flip-flops
NEXT-STATE LOGIC
AND · OR · NOT
OUTPUT DECODER
Six lamp outputs
3

## Slide 4
LOGISIM IMPLEMENTATION
Logisim implementation mirrors the FSM blocks
Each clock step exposes one state, one decoded lamp pattern, and one safe transition.
Illustrative schematic — not an actual Logisim screenshot.
4
CLOCK
pulse
STATE REGISTER
3 D flip-flops
NEXT-STATE
AND · OR · NOT
OUTPUT DECODER
state → lamps
M R
M Y
M G
S R
S Y
S G

## Slide 5
Simulation results: one green road at a time
State | Meaning | Main R | Main Y | Main G | Side R | Side Y | Side G
S0 | Main green | 0 | 0 | 1 | 1 | 0 | 0
S1 | Main yellow | 0 | 1 | 0 | 1 | 0 | 0
S2 | Both red | 1 | 0 | 0 | 1 | 0 | 0
S3 | Side green | 1 | 0 | 0 | 0 | 0 | 1
S4 | Side yellow | 1 | 0 | 0 | 0 | 1 | 0
SAFETY CHECK
Main G = 1 and Side G = 1 never occur together.
Clock edge + current state determine the next state and lamp pattern.
SIMULATION EVIDENCE
[Insert real Logisim simulation screenshot here]
Do not label the illustrative schematic as a screenshot.
5

## Slide 6
CONCLUSION
The controller is simple, safe, and ready to extend
Simple and safe
The FSM converts clock pulses into a predictable traffic-light sequence with an all-red clearance state.
Logisim makes the state register, combinational logic, decoder, and LED outputs easy to inspect and explain.
Applications: road intersections, campus traffic systems, and digital logic education.
Future improvements: vehicle sensors, adjustable timers, pedestrian buttons, and emergency-vehicle priority.
EXPECTED OUTCOME
A working simulation that demonstrates controlled traffic flow without simultaneous green signals.
Thank You
6